## Slide 1
5 Whys
(Root Cause Analysis)
Problem
How to find a problem’s root cause?
Ensure the problem is clearly articulated.
Ask “Why did the problem occur?” There may be several reasons.
For each of the reasons, ask “Why?”; each may have several reasons.
Continue asking “Why?” until the reasons are no longer actionable.
The lowest level reasons that are actionable are the root causes. If these are addressed then the problem should be resolved (or mitigated).
5 Whys
Process
Problem to resolve
Root cause(s)
The “5 Whys” technique is a simple & fast way to determine the root cause(s) of a problem.
The question “Why?” is repeatedly asked, starting at the problem statement. The process stops when the results are not actionable; this often occurs after 5 “Why?” steps.
Difficulty
Easy to use
Copyright © 2022 Dan Zwillinger. All rights reserved.
Updated: 202210
1

## Slide 2
5 Whys – Example – Broken machine
Copyright © 2022 Dan Zwillinger. All rights reserved.
Problem: A specific machine is not working
Why #1
Reason: The drive belt is broken
Sub-reason: The drive belt was too dry
Sub-reason: Too much force on the belt
Sub-reason: The drive belt was not lubricated
Sub-reason: There was no oil in the machine
Sub-reason: The machine was not maintained according to manufacturer specifications
Sub-reason: The maintenance manual is missing
While this sub-reason could be followed with more “Whys”, as a machine user (and not the machine manufacturer) we are unlikely to be able to affect the machine design. Hence, this branch is not likely to be actionable.
Why #2
Why #3
Why #4
Why #5
Why #6
Sub-reason: No one was tasked to maintain the machine
This is a root cause.
This is a root cause.
Sub-reason: There was no oil in the warehouse
2
Why #6

## Slide 3
5 Whys – Notes
Slide 1
Slide 2
A 5 Whys analysis can be performed by a single person or a team.
A 5 Whys analysis is best done using sticky notes, so they can be re-arranged as needed.
It is never the case that “lack of <something>” is a root cause. There is always a reason why a specific thing did not occur.
Be careful with cause and effect. Each lower level reason, if mitigated, should mitigate the higher level reason from which it is derived.
It may not take “5 Whys” to get to root cause, it may only take 4 Whys or it may take 6 or more Whys.
Note that some branches can/should be pruned when they are not actionable.
Note that the “lack of oil” is not a root cause. In this case, it is flowed down to “not maintained …” & “no one tasked …”
Copyright © 2022 Dan Zwillinger. All rights reserved.
3