## Slide 1
Control Chart
Problem
How to monitor defects?
Determine which of 7 types of control chart to use (see example). The choice depends on
  data type, whether it is continuous or discrete
  sample size, whether or not it is constant
  type of analysis to be performed
Collect the data
Perform needed computations
Plot the results of the computation
Analyze the plots – look for a large variance or unusual patterns.
Control Chart
Creation
Existing process
State of the process
Copyright © 2022-2025 Dan Zwillinger. All rights reserved.
A Control Chart shows how a process evolves over time. It is used to monitor, control, and/or improve a process.
A Control Chart includes a
  center line (average)
  and the data boundaries
  Upper Control Line (UCL)
  Lower Control Line (LCL)
The UCL and LCL are three standard deviations above and below the center line.
Process in “statistical control” if data is between UCL & LCL.
Difficulty
Some training required
There are 7 control chart types
Discrete data: c, np, p, u
Continuous data:
Individual Moving Range (I-MR) average-range (Xbar-R)
average-sigma (Xbar-S)
Constant sample size
c: count number of defects per unit
np: count number of nonconforming items
Proportion of nonconforming items
p: sample size may vary
u: large sample size variations

## Slide 2
Control Chart – Example – Shoe Production
Copyright © 2022-2025 Dan Zwillinger. All rights reserved.
Sample chart
Each chart reaches the same conclusion:
“Process is in control”
Sample chart

## Slide 3
Control Chart – Notes
Slide 1
Slide 2
The control chart (also called a Shewhart chart or a process behavior chart) was invented by Walter A. Shewhart.
Control charts show the Voice of the Process (VoP); see the 6in6 on Voice of the Customer.
While a process in statistical control has consistent performance; it does not necessarily meet customer expectations. See the 6in6 on Statistical Process Control (SPC).
While analysis formulas are easy to find and use, using a statistical software package is recommended.
Control Chart guidelines
  While customers create specification limits, the UCL and LCL are computed. Specification values are never shown on a control chart.
  For an unchanging process, the UCL and LCL values are not changed.
  If a computed LCL value is negative, replace it with the value zero.
  Ensure that enough data is collected to make decisions; software packages will indicate when not enough data has been obtained.
This example shows what the 7 different types of control charts represent.
The example is for shoe production and indicates the different types of defects that might be interest:
  variation in a continuous value (such as shoe length), or
  variation in a discrete value (such as number of bad stiches per shoe, or the number of defective shoes).
For discrete data, a single chart is created. For continuous data, two charts are created (one for the mean of the process and one for the standard deviation of the process).
Copyright © 2022-2025 Dan Zwillinger. All rights reserved.
Recommended web sites for additional information
https://bootcamp.umass.edu/blog/quality-management/ultimate-guide-to-six-sigma-control-charts
https://sixsigmastudyguide.com/control-charts-study-guide/