## Slide 1
Design of Experiments (DOE)
Problem
How to determine the factors controlling an output?
Define the test objective(s)
  What is the overall problem?
Select and quantify the critical response(s)
  What observables are of concern?
Design the experiment (incorporate features such as randomization, replication, and blocking)
  Define all the inputs for each test
Perform all the tests and collect the data
Analyze the data (use a SW package)
Interpret the results
Verify the predicted outcome
DOE
Methodology
Experimental needs
Experimental
design
Difficulty
Work with an SME
Copyright © 2022 Dan Zwillinger. All rights reserved.
Design of Experiments (DOE) is a cost effective statistical approach that quantifies the effect of inputs on outputs.
DOE makes specific changes to inputs and observes the resulting outputs.
Constraints
Specific product or process
Y1
Y2
X1
X2
X3
Observables of interest
Controllable inputs
Terminology
Each input has “levels” (perhaps 3 different values for X1 and 4 different values for X2).
A “full factorial design” has a test for every possible combination of levels.
A “partial or fractional factorial design” uses a subset of the tests in the full factorial design.
This is the system
Problem – find inputs to minimize (say) the observables, using as few tests as possible.
Solution – use the model below – observables depend on the inputs, with (usually) the earlier terms being more important than later terms:
main effects
Two-way interactions
overall mean

## Slide 2
DOE – Example – Golf score
Copyright © 2022 Dan Zwillinger. All rights reserved.
(1) Want to minimize a golf score based on the following 7 controllable inputs. (Note that each input has 2 levels.)
(2) A full factorial seven factor design at 2 levels has 27=128 experiments. Instead, use 8 experiments:
Observed values go here
(3) Convert to input levels and perform the experiments. Potential observable values are shown.
(4) A simple analysis finds the most important inputs (to leading order) – these cause the largest change.
Example from: Jack B. ReVelle, Manufacturing Handbook of Best Practices: An Innovation, Productivity, and Quality Focus, https://books.google.com/books?id=_EfMBQAAQBAJ&pg=PP5

## Slide 3
DOE – Notes
Slide 1
Slide 2
The goal of DOE is to obtain useful results using a minimal number of tests.
Inputs are also called “factors”.
Use SMEs and SW tools to find a test plan.
The tests should be designed to capture the expected terms that are important in the input/output relationship – which may be the linear terms (the first term after the constant) or the higher order terms (the later terms)
The "one factor at a time" approach is inefficient compared to changing multiple factor levels simultaneously.
Usually, an initial “screening design” is used to reduce a long list of potentially important factors and interactions to only a few important effects.
Selecting or creating an appropriate partial or fractional factorial design
  depends on how many terms in the model are anticipated to be important
  depends on many other factors, such as possible relationships between the inputs
  is something of an art!
In this example the golf score is to be minimized.
The chosen design has only 8 tests; this is far fewer than the 128 in the full factorial design. For this example, that few tests may be adequate.
  The resulting predictions, that drinking and golf cart usage are the most important factors, should be verified
Note that, for the tests performed, each level for each input appears exactly four times.
Copyright © 2022 Dan Zwillinger. All rights reserved.