## Slide 1
Design Verification Plan and Report (DVP&R)
Problem
How to document a product’s acceptability?
Difficulty
Some training required
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.
If not available, create the product’s planned tests:
  Articulate the product’s functionality.
  Define discrete and actionable functionality tests for the anticipated environments
Create a Design FMEA for the product to identify failure modes not detected in the planned tests.
Create the Design Verification Plan (DVP)
  Include the planned tests.
  Include tests to address the deficiencies identified by an FMEA.
Perform the tests in the DVP and document the results in the DVR.
If needed, use the DVR results to update the DVP and repeat the process.
Create the DVP&R and file appropriately.
DVP&R
Process
DVP and DVR
Existing product or system
The Design Verification Plan (DVP) documents the strategy used to verify that a product (or system) meets its requirements (e.g., design specifications).
The Design Verification Report (DVR) documents the test results obtained by using the DVP.
A Design Verification Plan and Report (DVP&R) combines the DVP and the DVR.
A DVP&R may be used for legal or product “sell off” purposes.
A DVP&R has no standard format.
DVP&R

## Slide 2
DVP&R – Example – Automobile Radar
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.
Heading
part info
dates
Verification Plan
Verification Report
Details of every test performed : test start & end times, results, comments, …
Details of every test planned: test name, test method or procedure, test equipment, test performance (e.g., sample size and acceptance criteria)

## Slide 3
DVP&R – Notes
Slide 1
Slide 2
The purpose of a DVP&R is to manage and document the tasks needed to ensure a product meets its requirements.
A DVP&R is useful for investigating quality issues during a product’s life.
A DVP&R keeps track of
  tests that have passed or failed
  progress & issues that may arise
A DVP&R helps a manufacturer know the status of a product at every stage of development.
A Design FMEA defines the "what" and the DVP&R defines the "how".
V&V definitions
  Verification: Did you design the device right?
  Validation: Did you design the right device?
The basic elements of every DVP&R are shown in this example.
There are many formats for a DVP&R.
There are several software packages that can create a DVP&R.
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.