## Slide 1
Failure Mode Effects and Analysis (FMEA)
Problem
How to anticipate and mitigate potential problems?
Difficulty
Some training required
Copyright © 2022 Dan Zwillinger. All rights reserved.
Updated: 202210
FMEA is a systematic, proactive method for evaluating a process
to identify where and how it might fail and
to assess the relative impact of different failures
in order to identify where the process must be changed
FMEAs should be created whenever a failure can result in harm.
FMEA types include:
Design (DFMEA) focuses on components and subsystems
Process (PFMEA) focuses on manufacturing and assembly processes
Process
Determine FMEA type: Defect (FMEA), Design (DFMEA), or Process (PFMEA) and obtain appropriate standardized tables
Identify potential failure modes.
For each failure mode, using standardized tables, assess the following on a 1-10 scale:
    Severity rating (how bad it is, if it occurs)
    Occurrence rating (how often it will occur)
    Detectability rating (how likely it is to be detected, if it occurs)
For each failure mode, multiply the above three numbers (each 1 to 10) to obtain a Risk Priority Number (RPN)
For the failure modes with the highest RPN values, determine mitigation strategies
Failure Mode Effects and Analysis (FMEA) Process
Risk reduction strategies
System to be analyzed
1
Prioritized list of failure modes
Planning Documents
Process owners

## Slide 2
FMEA – Example – Giving a 6in6 presentation
Copyright © 2022 Dan Zwillinger. All rights reserved.
For simplicity, instead of using values 1 to 10 for {S,O,D}, use {1,3,9} for {low, medium, high}. The values in the grid match the words used.
RPN value is the product of the S, O, D values
Low RPN values do not need mitigation strategies
Comprehensive list of failure modes
High severity – which is bad – gets a ‘9’. High detectability – which is good – gets a ‘1’
Automobile Industry Action Group (AIAG) created the following standards for the North American auto industry
Severity
Detectability
Likelihood / Occurrence
2

## Slide 3
FMEA – Notes
Slide 1
Slide 2
For a given process, FMEA uses a weighted decision matrix to identify potentially high risk problems.
The risks – and there can be hundreds – are prioritized so that only the most important ones need to be addressed.
Three values are determined that charactreize each risk; they are multiplied together to obtain the RPN. The RPN values are then ordered, largest to smallest.
Different industry groups have determined appropriate {S, O, D} value for their industry.
  For AIAG, the “Occurrence” value is ’10’ if it happens more than half the time, but a value of ‘4’ if it occurs 1 time in 2,000 potential occurrences.
Risks with low RPN values may not need to be mitigated.
The mitigations identified should be implemented before the process is rolled out.
Copyright © 2022 Dan Zwillinger. All rights reserved.
3