## Slide 1
Pugh Matrix
Problem
How to choose among multiple alternatives?
Difficulty
Some training required
Copyright © 2022 Dan Zwillinger. All rights reserved.
The Pugh Matrix is a simple technique for making a decision among multiple alternatives.
The Pugh Matrix uses pairwise comparisons between the alternatives, for each defined criteria or requirement.
The most time-consuming part of using a Pugh Matrix is creating the selection criteria.
  The assessments are quick and the calculation is easy.
Process
Choose the alternatives to be compared
  List them along the top of the matrix.
Define the multiple selection criteria
  These are the “Critical to Quality” (CTQ) factors.
  They might come from the Voice of the Customer (VOC).
  List them along the left side of the matrix.
  Optionally, define weights for each CTQ (adding up to 1).
3. Define one of the alternatives as the Reference Design.
4. Have a team assign values for each alternative for each CTQ:
  Compare each alternative to the Reference Design.
  Assign one of the following values:
    0: alternative is comparable to the reference design
    +1: alternative is better than the reference design
    –1: alternative is worse than the reference design.
6. Calculate the score for each alternative, by adding the values.
  Optionally. weight each {-1,0,1} by that CTQ’s weight.
Pugh Matrix analysis
Preferred alternative
Alternatives
Critical to Quality Factors

## Slide 2
Pugh Matrix – Example – Buying a car
(3) Weighted case: each criteria has a weight
(6) Best alternatives
Weighted: 4 is highest value
Unweighted: 0.7 is highest value
(5) Computation using weights is an inner product:
0.3 = 0.2*(-1)+ 0.1(0) + 0.1*(-1)+0.1*(1)+0.2*(1)+0.3*(1)
(4) Computation when not using weights is a column sum:
1 = (-1) + (0) + (-1) + (1) + (1) + (1)
(1) Reference Design
(2) Team created comparison values
Copyright © 2022 Dan Zwillinger. All rights reserved.

## Slide 3
Pugh Matrix – Notes
Slide 1
Slide 2
The Pugh Matrix was invented by Stuart Pugh.
The values in the matrix do not need to be {-1,0,+1}, other commonly used values are {1,2,3} . The values can be used to indicate the amount of difference from the Reference Design.
Best practices:
  Carefully choose the evaluation criteria.
  A weighted Pugh matrix is usually more appropriate than an unweighted one – carefully choose the weights aligned with the customer needs.
  Use a diverse team of 4-8 people to determine the values.
  Document the value discussions.
Common failures
  Incorrect selection criteria
  Incomplete selection criteria
  Unclear selection criteria
The example shows the same data evaluated using both a weighted and an unweighted Pugh matrix – the conclusion (best alternative) is the same in each case.
The computation for the unweighted Pugh matrix is very simple, just add up the {-1,0,1} values for each alternative.
Copyright © 2022 Dan Zwillinger. All rights reserved.