## Slide 1
Statistical Process Control (SPC)
Problem
How to ensure process quality?
Statistical Process Control (SPC) is the application of statistical methods to the monitoring & control of a process to ensure that it produces conforming products
SPC involves collecting data, controlling a process through data charting and analysis, and understanding process capability.
Define the objectives for a specific process
Plan data collection points
Plan data analysis method
Understand & improve measurement system (see 6in6 on Gage R&R)
Collect & review data
Calculate control limits
Monitor & correct process based on data collected (see 6in6 on Control Charts)
Determine process capability (Cp and Cpk, see 6in6 on Process Capability)
Iterate process
Statistical Process Control Process
Process to be controlled
Understanding and control of process via data
Difficulty
Work with an SME
Process data
SPC tools
Upper/Lower Control limits (not customer specification limits)
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.

## Slide 2
Statistical Process Control (SPC) – Examples
There are many ways to
Calculate control limits
Monitor & correct process via collected data
The “Western Electric rules,” which are only useful for hand analysis, are below.
Western Electric process
Step 0 – find the process’ sample mean (m) and standard deviation (s)
Step 1 – create symmetric control limits, using ±3s
Step 2 – define 3 “zones”
  Zone C  region within 1s of m
  Zone B  region between 1s and 2s of m
  Zone A  region between 2s and 3s of m
Step 3 – plot new data points as they arrive and look for certain patterns that may indicate a process is not in control. Some of these patterns are shown below.
Many other rules have been described:
There are 8 “Nelson rules” https://en.wikipedia.org/wiki/Nelson_rules
There are 6 “Westgard rules” https://en.wikipedia.org/wiki/Westgard_rules
There are 6 “Western Electric rules” for data analysis using a range (R) chart – different from an (m,s) chart. https://en.wikipedia.org/wiki/Western_Electric_rules
For discrete defect data, the different control charts are p, np, u, and c.
https://en.wikipedia.org/wiki/Western_Electric_rules
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.

## Slide 3
Statistical Process Control (SPC) – Notes
Slide 1
Slide 2
The use of software for SPC is highly recommended; many popular software packages have this capability.
SPC software should be used for monitoring a system in real-time.
For many of the patterns for the Western Electric rules, a physical rationale can be given why the system is not in control.
Rule #4 may indicate a systematic measurement system problem (i.e., bias).
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.