## Slide 1
Theory of Inventive Problem Solving (TRIZ)
Problem
How to identify ideas to solve a problem?
TRIZ is a problem-solving tool obtained from invention patterns in the patent literature.
TRIZ’s approach is that a solution, for something close to your problem, has already been found. The goal is to find that solution and adapt it to your problem.
Modern TRIZ uses “76 standard solutions.”
(OLD) TRIZ – easier to describe & illustrate – identified technical & physical contradictions involving “39 universal features.” All solutions are then one or more of the “40 inventions.”
Create a specific problem statement.
  Identify a contradiction among the 39 universal features. That is, identify contradiction between features (A) and (B).
Create generic problem statement:
  Want to change (A) yet (B) deteriorates
Use contradiction table to identify which of the generic solutions, among the 40 invention principles, eliminates the contradiction
Brainstorm the generic solutions to create potential solutions for your problem
Evaluate the potential solutions
(OLD)
TRIZ
Process
Problem with “contradictions”
Solution concepts
Difficulty
Work with an SME
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.
39 Universal Features
1. Weight of moving object
2. Weight of stationary object
3. Length of moving object
4. Length of stationary object
5. Area of moving object
6. Area of non-moving object
7. Volume of moving object
8. Volume of stationary object
9. Speed
10. Force
…
38. Extent of automation
39. Productivity
40 Invention Principles
1. Segmentation
2. Taking out
3. Local Quality
4. Asymmetry
5. Merging
6. Universality
7. Nested doll
8. Anti-weight
9. Preliminary anti-action
10. Preliminary action
…
39. Inert atmosphere
40. Composite materials
Specific solution

## Slide 2
TRIZ (OLD) – Example – Improving a Beverage Can
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.
(1) Problem: Want to improve can wall thickness subject to undesirable effect of stress on can wall
A=("#4, length of a stationary object“)
B=("#11, stress“)
(2) Look up (#4,#11) in universal “contradictions table” (upper left corner shown below) to find applicable invention principles: {1, 14, 35}
1  Segmentation
14  Spheroidality
35  Change physical or chemical properties
(3) For each invention principle, look up description for inspiration. For example:
(4) Brainstorm on each of the 3 suggested invention principles to determine a solution.
#1 Segmentation Principle
  Make the can wall corrugated – increases material for the same burst strength.
#14 Spheroidality Principle
  Remove corners from the can, make it with rounded walls or make it a sphere – reduces material for the same burst strength.
#35 Change physical or chemical properties
  Make the can out of a stronger or lighter material. Changes amount of material needed, and weight, for the same burst strength.
Invention principle #1: Segmentation Principle
Divide an object into independent parts.
  Replace mainframe computer by personal computers.
  Replace a large truck by a truck and trailer.
  Use a work breakdown structure for a large project
Make an object easy to disassemble.
  Modular furniture
  Quick disconnect joints in plumbing
Increase the degree of fragmentation or segmentation.
  Replace solid shades with Venetian blinds.
https://commons.wikimedia.org/wiki/File:Soft_Drink.svg
https://commons.wikimedia.org/wiki/File:Titanium.svg
Cell at (row 4, column 11) has 3 entries: invention principles {1, 14, 35}
(5) Possible results
or
or

## Slide 3
TRIZ – Notes
Slide 1
Slide 2
TRIZ was invented by Genrich Altshuller and his colleagues, beginning in 1946.
The main value of TRIZ is that it can speed up the process of finding solutions to complicated problems.
Benefits of TRIZ
  You don’t need to reinvent the wheel
  Quicker path to solution
  Based on engineering solutions
Among all the TRIZ tools, contradiction analysis is the most frequently used method to address problems needing to eliminate a problem’s contradictions.
TRIZ assumes that every technological system follows the same "evolutionary laws.” There are 9 laws in 3 categories of laws: Static, Kinematic, and Dynamic.
ARIZ (algorithm of inventive problems solving) is a 9 step process with about 85 procedures to solve contradictions. It improves on other TRIZ tools (e.g., Sufield analysis, 40 inventive principles). It is challenging to describe in a few sentences.
The straightforward steps shown are for OLD TRIZ
  Identify contradictions of universal features
  Use the contradictions table to find potential solutions
  Brainstorming using those potential solutions
The problem statement said “Improve can wall thickness” – which could mean increasing or decreasing the material used in the can wall.
Copyright © 2022-2024 Dan Zwillinger. All rights reserved.